Версия для печати Нажмите сюда для просмотра этой темы в оригинальном формате

Форум на Исходниках.RU > Электроника и схемотехника > Зачем компьютерному БП напряжение -12В, -5В?

Автор: Сергей85 11.10.19, 14:54

Если возможно, со ссылками литературы. Из инета: -12В - для питания ком-портов и опер-усилков в составе звуковухи. -5В - для шины ИСА.

Автор: amk 12.10.19, 19:22

Про -12В ты сам нашёл. А -5В сохраняется видимо для совместимости. Вообще, -5В требовался старым микросхемам nМОП (i8080, КР580)

Автор: Pavia 13.10.19, 09:24

12 В нужно жесткому диску чем больше напряжение тем быстрее вращается его шпиндель. А так же быстрее колеблется головка.

Автор: Pavia 13.10.19, 11:50

Источник: https://www.datasheetarchive.com/pdf/downlo...tic%2520diagram

Автор: Prince 13.10.19, 13:36

В спецификации АТХ 2.2 линия -5В отсутствует. В какой версии ее исключили - не знаю.

Автор: Pavia 13.10.19, 15:01

Цитата 1.2 Jan, 2002 · Section 3.2.3 Typical Power Distribution. Change +5V loading on all power supplies distribution tables defined in DG to 0.3A · Section 3.3.2 PS_ON# . Add text “The power supply should not latch into a shutdown state when PS_ON# is driven active by pulses between 10ms to 100ms during the decay of the power rails.” · Section 3.2.3.2 Remove –5V from all power distribution tables. https://www.arxvaldex.com/pb/files/manuals/ATX12V_1_3dg.pdf

Powered by Invision Power Board (https://www.invisionboard.com)

© Invision Power Services (https://www.invisionpower.com)